Department of Health and Ageing guidelines on current video conferencing protocol standards

According to current Department of Health and Ageing guidelines, the equipment or software should comply with the following minimum standards:1

- H.323 Videoconferencing and/or

- SIP Videoconferencing

The following technical protocols are used by the equipment to provide interoperability:

- H.225 – Call Signalling, Registration, Admission and Status (RAS)

- H.245 – Control Signalling

- RTP/RTCP – Transmission of audio and video traffic

- H.460 – Firewall traversal

- H.239 – dual stream video conferencing capability

Video codecs

H.261, H.263, H.263+, H.263 Interlaced, and H.264

Audio codecs

G.711, G.722, G.722.1, G.728, G.729 including Annex A and B, G.723.1, G.722.1 (Annex C), AAC-LD, and AAC-LC

Encryption

- Advanced Encryption Standard (AES)

- Secure Real-Time Transport Protocol (SRTP) for SIP encryption

- Department of Health and Ageing. Guidance on security, privacy and technical specifications for clinicians. Draft for consultation Canberra: National Health Chief Information Officer Forum, Telehealth Cross Jurisdictional Telehealth Reference Group; 2011 [updated 15th September; cited 2011 15th September]; 31 August. Available at www.mbsonline.gov.au/internet/mbsonline/publishing.nsf/Content/connectinghealthservices-technicalstandards